- Drainage-channel BG-FILCOTEN pro NW 200 made of FILCOTEN HPC (high-performance concrete)

with integrated edge made of galvanised steel, stainless steel 1.4301 or cast iron,

load-class A15 – E600 kN, according to EN1433 – CE-certified,

channel joint with safety seam, sealable,

length 1000 mm, without or with 0,5 % slope

Building biology tested and recommended by IBR (Institut für Baubiologie Rosenheim, DE)

Fire-behaviour class: A1 according to EN13501 - non-combustible

100% recyclable with U-A marking

Delivery and installation according to the manufacturer's installation instructions.

NW/No.:		LxWxH: [mm]		weight: [kg]	eco-indicator: [kg]

Galvanised steel edge:

200 No. 0:		1000x238x265		44,0		CO2-Eq. 16,0

200 No. 20-0:		1000x238x365		64,4		CO2-Eq. 21,7

200 No. 1-10:		1000x238x265-315	44,5-53,9	CO2-Eq. 16,2-19,6

Cast iron edge:

200 No. 0:		1000x238x265		45,0		CO2-Eq. 18,7

200 No. 20-0:		1000x238x365		65,6		CO2-Eq. 24,4

200 No. 1-10:		1000x238x265-315	45,5-54,9	CO2-Eq. 18,9-22,8

Stainless steel edge:

200 No. 0:		1000x238x265		44,0		CO2-Eq. 14,0

200 No. 20-0:		1000x238x365		64,4		CO2-Eq. 19,7

200 No. 1-10:		1000x238x265-315	44,5-53,9	CO2-Eq. 14,2-17,2

- Drainage-channel as described in position 1, but

overall length 500 mm, without slope

NW/No.:		LxWxH: [mm]		weight: [kg]	eco-indicator: [kg]

Galvanized steel edge:

200 No. 0:		500x238x265		22,1		CO2-Eq. ca. 8,1

200 No. 5-0:		500x238x290		29,6		CO2-Eq. ca. 10,8 	(plain sidewall)

200 No. 10-0:		500x238x315		27,0		CO2-Eq. ca. 9,9

Ductile iron edge:

200 No. 0:		500x238x265		22,6		CO2-Eq. ca. 9,4

200 No. 5-0:		500x238x290		30,1		CO2-Eq. ca. 12,5 	(plain sidewall)

200 No. 10-0:		500x238x315		27,5		CO2-Eq. ca. 11,5

Stainless steel edge:

200 No. 0:		500x238x265		22,1		CO2-Eq. ca. 7,1

200 No. 5-0:		500x238x290		29,6		CO2-Eq. ca. 9,5 	(plain sidewall)

200 No. 10-0:		500x238x315		27,0		CO2-Eq. ca. 8,6

- Surcharge for bottom outlet DN 200,

for drainage channels without slope

- Covers/Grates made of galvanised steel, stainless steel 1.4301 or cast iron with integrated longitudinal movement

protection and fiX-lock or 4-fold screw connection, load class A 15kN – E 600kN, according to EN1433 - CE-certified

BG-FILCOTEN tec/pro mesh grating NW 200, galvanised steel or stainless steel

cl. C250, MW 30/10, length 1000 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN tec/pro mesh grating NW 200, galvanised steel or stainless steel

cl. C250, MW 30/10, length 500 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro mesh grating NW 200, galvanised steel or stainless steel

cl. D400, MW 25/10, length 1000 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro mesh grating NW 200, galvanised steel or stainless steel

cl. D400, MW 25/10, length 500 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN tec/pro perforated grating NW 200, galvanised steel or stainless steel

cl. C250, DM 6, length 1000 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN tec/pro perforated grating NW 200, galvanised steel or stainless steel

cl. C250, DM 6, length 500 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN tec/pro ductile-iron bar grating NW 200, ductile-iron EN-GJS

cl. C250, MW 29/13, length 500 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro ductile-iron bar grating NW 100, ductile-iron EN-GJS

cl. D400, MW 29/13, length 500 mm,

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro ductile-iron slotted grating NW 200, ductile-iron EN-GJS

cl. E600, SW 14/200, length 500 mm

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro ductile-iron design-grate „VIA“ NW 200, ductile-iron EN-GJS

cl. D400, SW 7, length 500 mm

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro ductile-iron design-grate „KIARO“ NW 200, ductile-iron EN-GJS

cl. D400, SW 7, length 500 mm

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

BG-FILCOTEN pro ductile-iron design-grate „VILLE“ NW 200, ductile-iron EN-GJS

cl. E600, SW 7, length 500 mm

with integrated longitudinal movement protection and fiX-lock, according to EN1433 - CE-certified

Anti-vandalism locking device made of stainless steel cross piece for blocking the fiX-lock

BG-FILCOTEN pro ductile-iron slotted grating NW 200, ductile-iron EN-GJS

cl. D400, SW 14/200, length 500 mm

with integrated longitudinal movement protection, 4-fold screw-connection (only in cast-iron edge), according to EN1433 - CE-certified, bolting material must be ordered separately, bolting material is exchangeable.

BG-FILCOTEN pro ductile-iron bar grating NW 200, ductile-iron EN-GJS

cl. E600, MW 22/13, length 500 mm

with integrated longitudinal movement protection, 4-fold screw-conection (only in cast-iron edge), according to EN1433 - CE-certified, bolting material must be ordered separately, bolting material is exchangeable.

KIT-bolting material for ductile iron grating

steel, black galvanised - consisting of 1 pc. screw and 1 pc. nut (requirement: 8 pcs./m)

KIT-bolting material material for ductile iron grating

stainless steel A2 - consisting of 1 pc. screw and 1 pc. nut (requirement: 8 pcs./m)

- sump unit kit BG-FILCOTEN pro NW 200 made of FILCOTEN HPC (high-performance concrete)

with integrated edge made of galvanised steel, stainless steel 1.4301 or cast iron, incl. silt bucket

outlet: pipe coupling DN 200

Länge 500 mm / width 265 mm / height 750 mm

Delivery and installation according to the manufacturer's installation instructions.

Galvanised steel frame: 48,7 kg

Cast iron frame:	 49,1 kg

Stainless steel frame: 	 48,7 kg

- front cap closed, made of galvanised steel or stainless steel 1.4301

weight: 0,8 kg

- end cap, with outlet DN200 made of galvanised steel or stainless steel 1.4301

weight: 1,1 kg

- installation chair, Kit incl. screws for positioning the channel, galvanised steel

weight: 1,7 kg